## Slide 1
DEPARTMENT OF ARTIFICAL INTELLIGENCE AND DATA SCIENCE
Project Team Members
Name USN
A.CHETAN KUMAR 1SJ22AD005
M.AKASH ROYAL 1SJ22AD021
Y.REVANTH REDDY 1SJ22AD063
Under the Guidance of
DARSHAN A
Assistant Professor
SMART FARMING SOLUTIONS FOR CROP DISEASE PREDICTION AND CONTROL USING IOT AND ML
Project Phase-2
Review 2

## Slide 2
TABLE OF CONTENTS
  Abstract
  Introduction
  Problem Statement
  Objectives
  Design
  Modules Split-up
  Implementation
  Testing
  Screen shots of output
  Conclusion and Future enhancement
  References
A Hybrid Neural Network for EEG-based Depression Screening

## Slide 3
A Hybrid Neural Network for EEG-based Depression Screening
ABSTRACT
Smart Farming Solutions for Crop Disease Prediction and Control using IoT and ML presents an intelligent system that integrates machine learning with IoT to enhance agricultural productivity and crop health management. An Arduino controller is interfaced with sensors such as soil moisture, pH, and DHT11 to monitor essential soil and environmental conditions. A USB web camera is used for real-time disease detection through image analysis, while a relay-controlled DC water pump automates irrigation when low soil moisture is detected. The system displays readings on an LCD and uses a buzzer to alert farmers during abnormal conditions. By combining IoT-based monitoring with machine learning algorithms, the system ensures accurate disease prediction, optimized irrigation, and timely farmer intervention, thereby reducing crop loss and increasing yield efficiency.

## Slide 4
Agriculture is a vital sector that requires efficient crop management to maximize yield and minimize losses. Traditional farming methods, which rely heavily on manual monitoring, are often time-consuming and prone to errors. To address these challenges, the project “Smart Farming Solutions for Crop Disease Prediction and Control using IoT and ML” integrates Internet of Things (IoT) and Machine Learning (ML) to create an intelligent system for real-time crop monitoring and disease management. The system uses an Arduino controller connected to sensors such as soil moisture, pH, and DHT11 to continuously monitor essential soil and environmental conditions. A USB web camera captures crop images for disease detection through ML-based image analysis, while a relay-controlled DC water pump automates irrigation whenever low soil moisture is detected. An LCD displays real-time readings, and a buzzer alerts farmers to abnormal conditions requiring immediate attention. By combining IoT-based monitoring with ML-driven predictive analysis, the system enables early disease detection, optimized irrigation, and timely intervention, thereby reducing crop loss and enhancing overall agricultural productivity.
INTRODUCTION

## Slide 5
  PROBLEM STATEMENT
The agricultural sector, a pivotal cornerstone of economic stability and human sustenance , faces a persistent challenge in achieving optimal output because crops are frequently afflicted with diseases during their growth. The traditional method for addressing this issue relies on manual disease monitoring, which poses a formidable obstacle. This manual process is inherently inefficient, demanding substantial labor, specialized knowledge of plant pathology, and significant time. Consequently, diseases are often detected late, which impedes timely intervention and leads to poor crop production , exacerbated crop losses, and increased economic burdens.

## Slide 6
A Hybrid Neural Network for EEG-based Depression Screening
To combine machine learning (ML) and the Internet of Things (IoT) to predict and manage crop diseases and implement corrective actions.
To collect real-time data on crop conditions using IoT devices equipped with sensors for temperature, moisture, humidity, and integrate ML output with these readings.
To analyze environmental inputs using Random Forest classifiers to predict and categorize the environmental status.
To analyze live webcam footage using a YOLOv8 model to detect, classify, and compute the severity of rice leaf diseases in real-time.
To enable an Arduino controller to receive ML-based predictions and activate appropriate corrective actions.
To transform the farming process by providing farmers with a more precise and efficient way of managing and monitoring crops through the integration of IoT and ML.
OBJECTIVES

## Slide 7
A Hybrid Neural Network for EEG-based Depression Screening
DESIGN

## Slide 8
A Hybrid Neural Network for EEG-based Depression Screening
1. Data Collection and Preprocessing Module
Tasks:
  Collect leaf images (healthy & diseased)
  Label images into categories(Healthy, Fungal, Bacterial, Pest)
  Resize, normalize, and augment images
2. Machine Learning Model Development Module
Tasks:
  Import all necessary libraries (pandas, sklearn, serial, cv2, ultralytics, etc.).
  Establish a serial connection to the Arduino. Load the sensor dataset from data.xlsx.
  Train three Random Forest Classifier models, one for each sensor
MODULES SPLIT-UP

## Slide 9
A Hybrid Neural Network for EEG-based Depression Screening
4. Real-Time Disease Detection Module (YOLOv8)
Tasks:
  Load the custom-trained YOLOv8 model (best.pt).
  Define a function to open the webcam.
  Process video frames to detect and draw bounding boxes for diseases.
  Estimate the infection percentage and severity level for detected diseases.
  Display the live video feed with detection results.
5. Main Execution & Decision Logic
Tasks:
  Run an infinite loop to continuously read sensor data.
  Use the trained Random Forest models to predict the status of the live sensor values.
  Check the user's initial mode choice: If Mode 1, only run sensor predictions.
  If Mode 2, launch the YOLOv8 detection function in a separate thread.
  Communicate final decisions back to the Arduino via serial.

## Slide 10
A Hybrid Neural Network for EEG-based Depression Screening
  IMPLEMENTATION
Random Forest Architecture:
Input Layer: Receives preprocessed sensor readings as numerical feature vectors.
Bootstrap Sampling: Creates multiple random subsets of the training data for diversity.
Decision Trees Ensemble: Each tree independently learns classification rules using different feature subsets.
Voting Mechanism: Each tree provides a prediction; the final output is obtained by majority voting across all trees.
Output Layer: Produces the predicted class label — such as Healthy, Dry Soil, or Acidic pH — which can be used to trigger IoT actions (e.g., irrigation, fertilization).

## Slide 11
A Hybrid Neural Network for EEG-based Depression Screening
YOLOv8 Architecture:
Input Layer: Captures live RGB images (e.g., 640×640 pixels) from the camera.
Backbone (CSPDarknet): Extracts multi-scale visual features using convolutional and residual (C2f) blocks.
Neck (PAN-FPN): Aggregates and refines features from different layers to detect both large and small lesions.
Head: Predicts disease class, bounding box coordinates, and confidence score for each detected region.
Post-Processing (NMS): Removes redundant overlapping boxes, keeping the most confident detections.
Output: Displays bounding boxes, disease labels, and infection severity levels in real time.

## Slide 12
TEST CASE
Test Case UTC01 - Serial Port Connection
Test Case# | UTC01
Test Name | Serial Port Connection
Test Description | To test if the program successfully connects to the Arduino on COM5.
Input | Arduino plugged into the correct USB port, identified as COM5.
Expected Output | The console should print: "✅ Serial connection opened successfully on COM5!"
Actual Output | The console printed: "✅ Serial connection opened successfully on COM5!"
Test Result | Success
Test Case UTC02 - ML Model Data Loading
Test Case# | UTC02
Test Name | ML Model Data Loading
Test Description | To test if the program can read the sensor data from the data.xlsx file.
Input | data.xlsx file is present in the script's root directory.
Expected Output | The console should print: "✅ Excel data loaded successfully!"
Actual Output | The console printed: "✅ Excel data loaded successfully!"
Test Result | Success

## Slide 13
Test Case UTC03 - Sensor Data Parsing
Test Case# | UTC03
Test Name | Sensor Data Parsing
Test Description | To test if the program correctly parses a valid, complete data string from the Arduino.
Input | Serial string received from Arduino: a27.5b650c6.8d
Expected Output | The program should parse and print the individual float values correctly.
Actual Output | Program printed: temperature : 27.5, soilStatus : 650.0, phValue : 6.8
Test Result | Success
Test Case UTC06 - YOLO Disease Identification
Test Case# | UTC06
Test Name | YOLO Disease Identification
Test Description | To test if the YOLOv8 model correctly identifies a disease from the live webcam feed.
Input | A leaf with "Bacterial Leaf" disease is shown to the webcam.
Expected Output | The video feed should display a bounding box over the leaf labeled "Bacterial Leaf" with a severity estimate.
Actual Output | The video feed displayed a box labeled "Bacterial Leaf (38.5%)" and "Severity: Medium".
Test Result | Success

## Slide 14
  CONCLUSION
The Smart Farming Solutions for Crop Disease Prediction and Control using IoT and ML project demonstrates an effective approach to modern agriculture by integrating real-time monitoring, automation, and predictive analytics. By utilizing sensors to track soil and environmental conditions, a USB camera for disease detection, and a relay-controlled irrigation system, the project ensures timely intervention and optimized resource usage. The combination of IoT and machine learning allows for accurate disease prediction, efficient water management, and prompt alerts to farmers, ultimately reducing crop losses and improving yield. This intelligent system highlights the potential of technology-driven solutions in enhancing agricultural productivity, promoting sustainable farming practices, and supporting farmers in making data-driven decisions.

## Slide 15
A key advancement involves integrating Edge AI by replacing the PC-dependent setup with a Wi-Fi-enabled microcontroller such as the ESP32, enabling independent operation and cloud connectivity. The YOLOv8 model can be deployed on an edge-AI platform like the Raspberry Pi 5 or Jetson Nano for real-time, on-field analysis. This setup would support closed-loop automation, such as activating a water pump or pesticide sprayer based on AI predictions. A multi-variate Random Forest Classifier could enhance decision-making by learning complex correlations among sensor parameters, while expanding the sensor suite with NPK, BME280, and light sensors would further enrich system intelligence. All data can be visualized in a centralized web or mobile dashboard for live monitoring and manual control.
FUTURE ENHANCEMENT